## Slide 1: Federal Environmental Policies Affecting Transmission & Storage
Kyle Danish
Energy Bar Association
Program on Natural Gas Pipeline Modernization
Mar. 12, 2024

## Slide 2: Key Drivers for Environmental Compliance Costs
PHMSA regulations
EPA’s “Good Neighbor” Rule
EPA’s “OOOO” regulations
Waste Emissions Charge

## Slide 3: Good Neighbor Rule: State of Play
Source: Clean Air Act requirement on all states to address ozone transport
EPA disapproved 22 state plans
  Imposed federal plans
Litigation morass
  In effect for 10 states
  Stayed in 12 states
  Emergency motion to stay entire rule under review in Sup. Ct.

## Slide 4: Good Neighbor Rule: Impacts on Compressors
May 1, 2026 compliance deadline for NOx standards
Requires retrofits to gas-fired reciprocating engines ≥ 1000 hp
INGAA estimates 1200 units affected
Reliability risk
Engines must be taken offline
Cannot confine work to shoulder months
Only 2 vendors

## Slide 5: EPA’s “OOOO” Regulations
Affected sources in T&S segment
Compressors stations
Pneumatic pumps
Pneumatic controllers
Storage vessels
Types of requirements
Equipment replacement
Process changes
Leak detection and repair (LDAR)

## Slide 6: “OOOO” Regulations: Timing
Sources newly-built or modified after Dec. 6, 2022
May 2024
Sources existing prior to Dec. 6, 2022
Federal-state process
State plans due: no later than May 2026
EPA approval process: in 2027
Compliance deadline under state plans: generally no later than May 2029

## Slide 7: “OOOO” Regulations: Selected Requirements
T&S Source | Requirements
Fugitive emissions at compressor stations | Monthly AVO surveys and quarterly OGI surveys with deadlines for repairing detected leaks.
Compressor stations | Wet seal: 95% reduction in emissions Wet seal (self-contained or mechanical seal): volumetric flow rate may not > 3 scfm/seal Dry seal: volumetric flow rate may not > 10 scfm/seal Reciprocating: volumetric flow rate no more than 2 scfm/cylinder
Process controllers (NG-driven) | Zero emission rate
Storage vessels with PTE of 20 tpy or more of methane | 95% reduction in emissions

## Slide 8: “OOOO” Regulations: Advanced Technologies
Operators may use EPA-approved technologies in lieu of OGI
Satellites
Aerial surveys
Continuous monitors
Third party “Super Emitter Program”
EPA-approved third parties using EPA-approved technologies
Notify EPA of “Super Emitter” events

## Slide 9: Waste Emissions Charge
Added by the Inflation Reduction Act
Implemented by EPA
Effective in 2025 for 2024 emissions
Applies to:
  “Affected facilities”
  Emissions in excess of statutory thresholds
Interaction with “OOOO” regulations

## Slide 10: Waste Emissions Charge: Affected Facilities
Affected facilities
Reporting in Subpart W of Greenhouse Gas Reporting Program
T&S Segment
Emit > 25,000 metric tons of CO2 equivalent/yr
Calculation of charge
For T&S facilities, charge applies to all reported tons of methane emissions in excess of 0.11% of gas sent to sale from or through facility
$900/t in 2024 / $1200/t in 2025 / $1500/t in 2026 and thereafter
Netting
An owner of multiple facilities may offset higher-emitting applicable facilities with lower

## Slide 11: Waste Emissions Charge: Regulatory Exemption
WEC applicable facility eligible for exemption if:
  “OOOO” regulations are approved and in effect in all states with WEC applicable facilities (projected 2027)
  All equipment/components at the facility are in compliance with the “OOOO” regulations

## Slide 12: Key Takeaways
Methane mitigation requirements are coming for the T&S segment
The requirements will reach new and existing facilities
The requirements vary in form and stringency
The requirements create incentives for advanced methane monitoring and measurement technologies

## Slide 13: For more information:
Kyle Danish
202-361-5621
kwd@vnf.com
@kyledanish